Mechanical notes
For the Dog Bowl Scale
Not to scale

---
Side view
Counterbored
holes
Nut
12.7mm
M5 bolt
Water
Curtain
To
Keep
Water
out
10mm
Sensor load end
Load Cell
12.7mm
Min 32mm
Center access hole,
enabling assembly or
removal of the top.
Threaded
spacer
10mm
M4 bolt
12.7mm
Nut
Assembly order: 1) thread bolts into load cell 2) thread spacers onto bolts 3) thread nut onto bolt. Thread the bottom nuts before the top nuts.
The load end bolts are in the center so they are roughly under the center of gravity of the water or food bowl. Be sure the Load Cell end with the smaller holes (the M4 end) has its arrow label pointing down.

---
Top View
Counterbore hole
Nut

---
Bottom View
Nuts that fasten
the top onto
the Load Cell
Flathead bolts
that screw into
the Load Cell
Access hole
Routed out path
for the USB cable
Note: bolt holes and counterbore holes for the other parts are not shown.

---
Top view of bottom parts – rough layout
Load Cell Amp
Load cell
Arduino
Note: the Arduino is as far left as possible, so that we can bend the USB cord
or power cord into a slot in the bottom. This slot is so that the cord goes outside
without dragging spilled water into the bottom parts.